## Slide 1
Foil Activation Experiments and Neutron Flux Unfolding
Lt Nick Quartemont
MS Nuclear Engineering 19M
Air Force Institute of Technology
8 Aug 18

## Slide 2: Overview
Motivation
Research Plan
Experimental Setup
Foil Activation Theory
Selection of Activation Foils
Neutron Flux Unfolding
STAYSL

## Slide 3: Motivation
Characterization of neutron energy spectrum
  Activate foils in experimental environment
  Unfold incident neutron spectrum from Nuclear Data and calculated activities to determine a representative result
Nuclear Data * Source Spectrum Foil Activities

## Slide 4: Research Plan
(24 July - 3 Aug ) Irradiate foils in Bld 470 pile for 10 days (Foils are In, W, Au, Mn, Al).
(24 July -03 Aug) Characterize HPGe in Rm 105
(03 Aug) Measure Al, Indium and Manganese Activation foils
(03 Aug – 06 Aug) Measure Tungsten and Gold foils
(2-9 Aug) Analysis and preparation for research update
(9 Aug) Research Update
(9-16 Aug) Draft Project Article
(9-21 Aug) Spectrum Unfolding Using STAYSL
(16-23 Aug) Create Lab Procedures
(21 Aug) Lab Notebook
(21-30 Aug) Final Project Article

## Slide 5: Experiment Overview
Experiment
HPGe
Multi-nuclide source Energy Calibration Efficiency Calibration
1 week
irradiation
Time Corrected Foil Activities

## Slide 6: Experimental Setup (Plan) - Irradiation

## Slide 7: Irradiation
- Planned 7 day irradiation
PuBe Source Energy Distribution Inside Pile

## Slide 8: Foil Neutron Environment

## Slide 9: Experiment Progress
Experiment
HPGe
Multi-nuclide source Energy Calibration Efficiency Calibration
1 week
irradiation
Time Corrected Foil Activities

## Slide 10: Foil Activation
Saturation Activity

## Slide 11: Foil Activation
Activity Post-Irradiation
Measured Counts Corrections
Short Irradiation Time

## Slide 12: Selection of Activation Foils
Neutron cross-section
  Magnitude (large enough to produce activity)
  Uniqueness ( threshold, resonances)
  Cover energy range of interest (thermal – 12 MeV)
Nuclear data (uncertainty)  IRDFF v1.05
Decay Constant (dependent on time until foils can be measured)
Elemental and chemical purity
Interfering reaction channels / decay emissions
  Natural Cu  multiple 511 keV emissions
  Cd-106 and Cd-108 (n,2n) both produce Cd-107
Activation foil must be optically thin
Decay nature of activation products are gamma emitters

## Slide 13: Selected Foils for Pile
All values under 1% Statistical Uncertainty
https://www.tablesgenerator.com/

## Slide 14: Neutron Flux Unfolding
=
Reaction Matrix [cm^2] Flux [n/cm^2-s] Reaction Rate [1/s]
If you knew everything… it is just doing a matrix inversion of the reaction group averaged cross-section.
(n,g)
(n,n’)
(n,2n)
(n,2n)

## Slide 15: Neutron Flux Unfolding
=
Reaction Matrix [cm^2] Flux [n/cm^2-s] Reaction Rate [1/s]
If you knew everything… it is just doing a matrix inversion of the reaction group averaged cross-section.
Does not work because:
Measurement Error
Too broad of bin structure (Can get thermal to fast ratio – Cd)
Adding too many foils to create a large bin structure is counter to being optically thin
(n,g)
(n,n’)
(n,2n)
(n,2n)

## Slide 16: Unfolding Solution Methods
Not a complete list (follows most optimization routines)
Matrix inversion
  Degeneracies
  Bad way
  Can lead to non-physical results
Least-square spectral adjustment (ex. PNNL STAYSL)
  Incorporates uncertainty
  Incorporates covariance
  Requires guess spectrum
    Degenerate solutions exist  Guess spectrum applies physics to constrain the end-point result.
    Monte Carlo, deterministic, “back of the envelope”, published results
Stochastic methods

## Slide 17: NIF Snout Foil Activation Experiment
Kinematic Base
Basket
Pinhole
- Compare deviations from
expected results

## Slide 18: NIF Snout Foil Activation Experiment
Difference from Pile experiment: sizes and Zr
Zr-90 (n,2n) Zr-89, 78 hr half-life, gamma 909 keV (0.9904)

## Slide 19: Following from HPGe Results

## Slide 20: PNNL STAYSL

## Slide 21: BCF / SHIELD
  BCF not used.
    NIF shot is 200 ps (longer when taking reactions into consideration).
    Does not impact results as the half-lives of measured products are comparatively long.
  SHIELD
    Calculates energy-dependent neutron self-shielding cross section correction factors that are used
    SHIELD is only necessary/valid on non-threshold reactions (n,gamma).

## Slide 22: STAYSL - Guess Spectrum

## Slide 23: SIG-PHI Guess Spectrum
Did not work for me
Excel macro/version issue

## Slide 24: Experimental Input to STAYSL

## Slide 25: Iterative Unfolding
  Start with guess spectrum
  Use evaluation from STAYSL as guess for new spectrum
  Start with 100% uncertainty in energy regions where little is known
  Constrain future iterations with error produced in mini-spectrum
  Run until chi-square has stabilized

## Slide 26: Pinhole Iterative Results
  Iteration 0 Iteration 6
  values point to this not being the correct flux spectrum
  Need a better starting spectrum
  Large error in Au-197 (n,g) limits results
  Error bars are output from STAYSL

## Slide 27: Questions